## Slide 1
MYZ307E
Machine Learning for EE
Istanbul Technical University
Spring 2025-2026
Team Members:
Muhammed Yasir KAMA — 040210361
Kaan KAYALIK — 040210443
Başar KARADAŞ — 040210435
Mert YİLMAZ — 040210366
TERM PROJECT
Power System
Fault Detection &
Classification
Using Ensemble Machine Learning Methods
Dr. Sümeye Nur Karahan

## Slide 2
Problem Definition & Motivation
Why this matters — and why ML?
⚡ The Problem
Transmission line faults (LG, LL, LLG, LLL,
LLLG) cause major outages if undetected
within milliseconds.
Traditional relay protection uses fixed
thresholds — not adaptive to modern
smart grid conditions.
3-phase current & voltage signals carry
learnable fault signatures that ML can
exploit without manual tuning.
🎯 Two-Stage Approach
Stage 1 — Detection
Binary: Normal vs. Fault
Dataset: 12,001 samples | 54.2% Normal / 45.8% Fault
↓
Stage 2 — Classification
6-class: Which fault type?
Dataset: 7,861 samples | 6 fault classes
No Fault
LG
LL
LLG
LLL
LLLG

## Slide 3
Reference Paper & GitHub Repositories
What we built upon — and their limitations
📄 Primary Reference Paper
T. Anwar, C. Mu, M. Z. Yousaf et al., "Robust Fault Detection and Classification via Ensemble ML Models" — Scientific Reports, Nature, 2025
DOI: 10.1038/s41598-025-86554-2 | RF-LSTM Tuned KNN ensemble → 99.96% accuracy
1 Repo 1 — svdeepak99
github.com/svdeepak99/Machine_Learning-Power_System_Fault_Detection
• SVM, Decision Tree, RF, PCA, GMM, MLP
• 12,001 samples — binary detection only
⚠ No classification — no ensemble
2 Repo 2 — KingArthur000
github.com/KingArthur000/Electrical-Fault-detection-and-classification
• MATLAB Simulink dataset, 7,861 valid samples
• Detection + classification attempted
⚠ Poly. regression for classification — inappropriate

## Slide 4
Dataset & Preprocessing
Real values from notebook output
Features (x ∈ ℝ⁶)
Ia
Phase A Current
Ib
Phase B Current
Ic
Phase C Current
Va
Phase A Voltage
Vb
Phase B Voltage
Vc
Phase C Voltage
Dataset 1 — Detection (powerline_dataset.csv)
12,001 samples • Binary: 0=Normal, 1=Fault • 6 features
Normal 54.2% (6505)
Fault 45.8% (5496)
Dataset 2 — Classification (classData.csv)
7,861 valid samples • 6 features • Multi-label [G,C,B,A] → 6 classes
No Fault
2365
LG
1129
LL
1004
LLG
1134
LLL
1096
LLLG
1133
⚙ StandardScaler (fit on train only) • 80/20 stratified split • PCA: 4 components → 96.9% variance

## Slide 5
Contributions (1/2) — Pipeline & Model Expansion
Baseline gaps and our solutions
✗ Baseline Gap
Repo 1: binary detection only —
no fault type classification
→
✓ Our Solution
Added 6-class classification stage using Dataset 2.
Unified two-stage pipeline: Detection → Classification.
✗ Baseline Gap
Repo 1 evaluates 5 models only.
Repo 2 uses polynomial regression
for classification — inappropriate.
→
✓ Our Solution
Evaluated 8 classifiers on both tasks:
+KNN, Naive Bayes, Logistic Reg., Gradient Boosting.
Replaced poly. regression with proper classifiers.
✗ Baseline Gap
No ensemble method in
either repository.
→
✓ Our Solution
VotingClassifier(RF + SVM + GB, voting='soft')
for both detection and classification tasks.

## Slide 6
Contributions (2/2) — Deeper Analysis
Analyses not present in either baseline
✗ Baseline Gap
GMM used with a single fixed
config in Repo 1 — not optimized.
→
✓ Our Result
Grid search over 32 configs (8×4).
Best: n_components=2, cov='full', threshold=6.9327.
Result: 98.08% detection without any fault labels.
✗ Baseline Gap
No feature importance analysis
in either repository.
→
✓ Our Result
Ablation study: removed each feature one-by-one.
Ia has largest impact (−0.17%). Ib removal slightly
improves (+0.04%) — correlated features.
✗ Baseline Gap
Single-dataset evaluation —
no cross-repository test.
→
✓ Our Result
RF trained on Dataset 1 tested on Dataset 2 binary
→ 99.94% accuracy. This suggests strong normal/fault pattern consistency across the two repository datasets, but real-world validation is still required.

## Slide 7
Results (1/2) — Fault Detection
Binary: Normal vs. Fault | All values from notebook output
Baseline (Repo 1 reproduced)
SVM (RBF)
~99.8% → 99.58%
Decision Tree
~99.8% → 99.58%
Random Forest
~99.8% → 99.63%
MLP
~98.0% → 99.5%
GMM
~99.5% → 98.08%
✓ Classical supervised baselines are close to reported values; MLP and GMM differ due to configuration and threshold changes.
Our Method — 8 Models + Ensemble
🏆 Voting Ensemble
99.75%
Gradient Boosting
99.67%
KNN (k=5)
99.67%
Random Forest
99.63%
SVM (RBF)
99.58%
Decision Tree
99.58%
MLP (ReLU+Adam)
99.50%
GMM (unsupervised)
98.08%
Naive Bayes
97.42%
Logistic Regression
71.30%

## Slide 8
Results (2/2) — Fault Classification
6-class: No Fault / LG / LL / LLG / LLL / LLLG | Notebook output
Baseline (Repo 2 reproduced)
SVM
(on clean repo data: ~99%)
Decision Tree
(on clean repo data: ~99%)
Random Forest
(on clean repo data: ~99%)
MLP
(on clean repo data: ~98%)
⚠ Our data: 7,861 valid samples
LLL/LLG confusion: LLL (F1=0.59) & LLLG (F1=0.59)
→ Three-phase faults have similar signatures
Our Method — 8 Models + Ensemble
🏆 Random Forest
88.24%
Voting Ensemble
87.48%
Decision Tree
85.76%
MLP (ReLU+Adam)
84.23%
Gradient Boosting
84.04%
SVM (RBF)
83.98%
Naive Bayes
79.40%
KNN (k=5)
79.28%
Logistic Regression
34.27%

## Slide 9
Analysis & Discussion
Why do the results look this way?
Why is detection (~99.75%) >> classification (~88%)?
Detection is binary — the model only needs to separate fault from normal current patterns. Classification must distinguish 6 fault types with similar 3-phase signatures. Confusion matrix confirms: LLL and LLLG are most confused (F1=0.59 each), as both are three-phase events.
Why does Ensemble beat individual models?
RF, SVM, GB learn via different mechanisms (bagging vs. margin vs. boosting). Their error patterns differ → soft-vote averaging cancels mistakes. Ensemble: 99.75% detection vs. best single model 99.67%.
What does the ablation study really show?
Removing Ia drops accuracy by 0.17% — the largest single drop. Removing Ib slightly improves (+0.04%), likely due to feature correlation. Result: current features matter, but all 6 features contribute to the ~99.6% baseline.
Why is GMM useful at 98.08% with no fault labels?
GMM trained only on normal samples forms tight clusters in 6D feature space. Fault conditions fall outside these clusters → threshold-based detection. Best config: n=2, cov='full', threshold=6.93. Practical for field deployment where fault data is scarce.

## Slide 10
Conclusions & Future Work
✅ Key Findings
🏆
Best Detection
Voting Ensemble (RF+SVM+GB): 99.75%
🔍
Best Classification
Random Forest: 88.24%
🌀
GMM Unsupervised
98.08% detection — zero fault labels needed
📉
PCA: 4 components
→ 96.9% variance with 33% dimension reduction
⚠️
LLL / LLLG
F1=0.59 — three-phase faults are hardest to classify
🔗
Cross-repo Check
99.94% — strong consistency across repository datasets
🔭 Future Work
Fault localization
Estimate distance on line
LSTM / Transformer
On raw time-series data
Address LLL/LLLG
Confusion with richer features
Real field data
Beyond Simulink simulation
IEEE benchmark
14/30-bus validation
Dr. Sümeye Nur Karahan • MYZ307E Spring 2025-2026 • M.Y.KAMA · K.KAYALIK · B.KARADAŞ · M.YİLMAZ